## Slide 1: Bluetooth proxy 044167 – Project A
Presented by Itay Zach & Avishay Shasha
Instructed by Eli Meirom

## Slide 2: Agenda
Motivation
Abstract
Goals
Technical background
Architecture
Full system demonstration
Timeline and validation
What did we learn?

## Slide 3: Motivation

## Slide 4: Motivation
Bluetooth is a standard protocol for short distance communication.
For some BT devices frequent adjustments are needed.
Since physical proximity is mandatory, these adjustments might be inconvenient.
  Medical area: hearing devices.

## Slide 5: Abstract
BT proxy project aims to overcome the BT physical proximity requirement.
Remote communication will be accomplished as follows:
  Windows and Android applications will be linked through TCP/IP.
  Bluetooth original data will be transacted through the link.
  Transparent to End User – nobody needs to leave the house! 

## Slide 6: Goals
Overcome BT’s need of physical proximity.
Create a proxy for the Bluetooth device and the end user.
Windows side
  Manipulate BT Windows API functions to create a TCP/IP communication through a hook using Microsoft Detours.
Android App side
  Android application will translate TCP/IP transactions to BT communication.

## Slide 7: Technical background
Function hooking using Microsoft Detours
  “Detours is a library for instrumenting arbitrary Win32 functions Windows-compatible processors. Detours intercepts Win32 functions by re-writing the in-memory code for target functions.”
  DLL injection method.
Windows Socket API
  Using the same API for different protocols.

## Slide 8: Detours demonstration

## Slide 9: Architecture

## Slide 10: Windows side
In the Windows Side we implemented an injector that injects a DLL containing the hooked WSA functions to the original executable.
BT and TCP sockets are opened.
  First, there is a connection attempt using BT in case no proxy is needed.
  If BT connection fails, the TCP connection is used.

## Slide 11: BT Proxy Android app
Resides in the user cell phone.
Acts as a tube between the Windows TCP client and the BT device.
Multithread app
  TCP server thread and BT client thread.
The TCP server waits for a TCP packet and the BT client transmits it to the device.

## Slide 12: Proof of concept
Dummy Windows application – BT client
BT Server Android application – BT device

## Slide 13
Full system demonstration

## Slide 15: Project planned timeline
Task | Description | Time approximation (Neto)
Win App <-> Android App TCP/IP |  | 2 weeks
Hook Win BT API for TCP/IP communication |  | 2 weeks
Create Android App <-> BT device BT communication |  | 2 week
Build destination detector | If BT device is near, use BT. If BT device is far, use TCP/IP. | 2 weeks
Integration |  | 2 weeks

## Slide 16: Project actual timeline & validation
Task | Method
Detours ramp up | Hook MessageBox API
Win App <-> Android App TCP/IP | Creating a TCP comm based on WSA
Hook Win BT API for TCP/IP communication | Based on Detours ramp up stage
Create Android App <-> BT device BT communication | BT client app and BT server app
Build destination detector | Was implemented during the Hook stage
Integration | Using proof of concept

## Slide 17: What did we learn?
BT communication protocol
Windows sockets
Advanced android programming
Using Microsoft Detours
Code revision control (GitHub)

## Slide 18: What’s next?
Project B
  Hooking up all remainder functions
  If time permits – cloud service

## Slide 19
Questions ?

## Slide 20: Gratitude and thanks
Eli Meirom
Roy Miterany
Victor Kulikov

## Slide 21: Thanks